BONNETS-WOOL BUFF PADS & ACCESSORIES

APPLICATION GUIDE

| Product Use | 4-Ply Twisted Wool | Terry Bonnet | Micro- Fiber Bonnet | Wool Polishing Blend | Other Wool | Wool Single Ply |
| --- | --- | --- | --- | --- | --- | --- |
| Compounding | X |  |  |  |  | X |
| Buffing* | X |  |  | X |  | X |
| Applying Wax |  | X |  |  |  |  |
| Removing Wax |  | X | X | X | X |  |
| Polishing |  |  |  | X | X |  |
| Swirl Eliminator |  | X |  |  |  |  |
| Pad Part Number | PAD1 880C 875D | R100 | M16 | 375PC 5705 | PP12 873 | 5703 |

*Buffing = Light Compounding

(See Reverse Side for Buff Pad Descriptions and Part Numbers)

##### Product Descriptions

| Part Number | Description |
| --- | --- |
| 5703 | 3M Superbuff( III Buffing Pad. A new 100%, double sided, wool pad with a stiffer central hub for more cutting power. This pad has untwisted yarn construction, which allows for more surface contact, while giving excellent cut and finish. Excellent for all paints and clears. |
| 5705 | 3M Superbuff( Polishing Pad This is a double sided, soft edge-polishing pad designed for use with a polisher and glaze. Superbuff™ polishing pad is made with extremely fine fibers to produce a high gloss on paint surfaces. Pad has its own built in, lightweight support system. |
| 5710 | 3M Superbuff( Adaptors. This adaptor has a 5/8-11 internal thread, which turns onto a polisher on one end, and a short 5/8-11 external thread on the other end. Used with Superbuff™ pads to keep the polisher shaft from hitting the car's paint finish. |
| 875D | 2” Pile Cutting Pad. 100% wool 4 ply twist is the most aggressive wool pad. Extra wool added for longer wear and more cushion. It is designed for any cutting application. Bolt on. |
| 880C | 1 ½” Pile Cutting Pad. 100% wool 4 ply twist is an aggressive wool pad. It is designed for any cutting application. Bolt on. |
| PAD1 | 1 ½” Pile Velcro Cutting Pad. 100% wool 4 ply twist is the most aggressive wool pad. It is designed for any cutting application. Quick change Velcro( backing system. |
| 375PC | Final Finish Velcro Pad. 1 ½” Pile. Yellow, wool and synthetic twisted 4-ply yarn. This polishing blend was developed for final finish and polishing. Perfect balance. This special blend performs excellent on today’s automotive finishes. Quick change Velcro( backing system. |
| 873 | Velcro Lambs wool. 100% pure wool is the absolute best when it comes to a finish that must be perfect. Sheepskin grip mounted pads. Quick change Velcro( backing system. |
| PP12 | Wool Polishing Pad. 100% wool knitted into stiff canvas back. Final polishing finish for autos and boats. Bolt on. |
| R100 | Terry Velour Bonnet. Professional quality. 100% cotton terry woven orbital bonnets. Terry on one side for buffing and polishing, Velour on the other for applying waxes. With elastic edge. Fits 10”-11” Orbital Machines. |
| M16 | High Pile Micro-Bonnet. Recommended for the professional. These long pile micro fiber terry bonnets are superior to all other bonnets. Its special fibers penetrate and absorb all particles to give a deep down shine without scratching. Used to remove waxes and polishes leaving a deep, clean shine. |
| C515 | GEM Orbital Drive Pads. Heavy-duty 11-inch diameter pads with pan. Perfectly balanced for your Orbital Polisher. |
| G500 | Meguiar’s Adjustable Buffer Handle. Revolutionary new adjustable-pivot buffer handle provides a more natural and comfortable wrist, arm and body position for improved control and reduced fatigue. Improves productivity and quality of work, as well as reduces chance of injury. For DeWalt, Black & Decker and other ½”-13 thread size buffers. For Makita use Part #A1 (Makita Adaptor) sold separately. |
| 7430525 | Makita Backing Plate. “Hook and Loop” surface makes changing Velcro( pads quick and easy. For use with Polishers with 5/8”-11 UNC Arbor. |
| 3704 | Kar Kraft Velcro Backing Plate. “Hook and Loop” surface for Quick Change Velcro( Pad System. For use with Polishers with 5/8”-11 UNC Arbor. |
| 711 | Professional Pad Cleaning Tool (Spur). A pistol grip tool with rotating spurs for easy cleaning of pads and bonnets. OSHA safe. |
| KKA | Kar Kraft Apron. Keep your appearance looking sharp. Prevent buffing splatter from staining your clothes. Tie back apron stamped with Kar Kraft Logo has convenient pockets for holding detailing brushes and polish/compound dispensing bottles. |